Authors: Angelica Amine, Mohamed Yassine Yahyaoui
Date : February 2021
UGE

ChatOS

Abstract

ChatOs is a discussion service between multiple Clients using the same server applying a predefined protocol without sharing users IP address.

Status of this Memo

This request for comment summarize the protocol to be implemented in the different packets used for communication between the user and other clients.
This document explains also the decisions behind the structure of the packets.

# 1. Introduction
ChatOs protocol purpose is to allow multiple and private communication between users without the need to expose their IP address, the protocol applied and described below is a simplified version of a chat server.

All the packets exchanged in this protocol use the Transmission Control Protocol, thus packets availability are handled by the operating system.

ChatOs allow three main operations :
- send a message to all the users
- send a message to a specific user
- start private connection with another user

To be able to use any operation, a connection with a server that uses the same protocol MUST be established beforehand.

## 1.1. Requirements notation
This document occasionally uses terms that appear in capital letters.

When the terms "MUST", "SHOULD", "RECOMMENDED", "MUST NOT", "SHOULD NOT", and "MAY" appear capitalized, they are being used to indicate particular requirements of this specification.

A discussion of the meanings of these terms appears in [RFC2119].

## 1.2. Terminology
We describe in this section the terminology used in the protocol.

UTF8
The UTF8 is set as the default charset used in ChatOS.
All requests and packets MUST use this charset unless	mentioned	otherwise in the RFC.

Request
A packet containing data sent from the client to the server.
Starts with request code, size of the ClientId followed by the
client ID, then the size of data zone followed by the data zone.
Ack
A response from the server to the client after receiving a	request.
Composed of a packet code of 1 byte, and a message zone of 126
bytes.

Packet Code
A code in the start of the packet, coded on 1 byte, indicates	the purpose or the state of the packet.

# 2. Connecting to the server and first requests
## 2.1. Connection to the server
The first step consists of a client connecting to the server.
For this, a client sends a connecting packet that follows this format :

1 byte 2 bytes	string
-----------------------------------------
| Code | NB | Pseudonym |
-----------------------------------------
Figure 2-1-1: Connecting Packet
The code represents the type of the packet that the server receive, in this case the code is “0” .
The nb field is an integer on 2 bytes which represents the size of the next field : the clientID , a string which is the pseudonym of the client.

To this request, the server returns an ACK packet to let the client know if connection was established successfully or not.

1 byte 126 bytes
---------------------------
| Code | MsgRetour|
---------------------------
Figure 2-1-2: ACK T1 Packet
The code field is an integer coded on 2 bytes which check if the received packet from the client is valid or not.
This field is followed by the message field which represents the reply of the server, we allow a fixed value of 126 bytes, to describe a short error/success message.
If the connection was successfully established then the code is “10”.
if the ClientID already used by another client, then the connection fails with the code “11”.
For any other errors that may occurs while connecting, the code “-3” is returned, with the return message specifying the cause .
## 2.2. Public message to all users

Once the client is connected to the server, it could either send a message to all users or specific one.
In this part, we are going to describe the process of sending a public message to all users.
For a “Client A” to send a message to all the other clients, he has to send a packet to the server following this format :

        1 byte 2 bytes TailleRec bytes 2 bytes TailleM bytes
        ------------------------------------------------------
        | Code | TAILLEREC | REC | TailleM | MSG |
        -----------------------------------------------------
Figure 2-2-1: DATA T1 Packet
The code field is an integer coded on 1 byte that tell the server “client A” is sending a message. The next field is the size of the receiver’s clientID
the REC MUST be the same size as TailleRec, the next 2 bytes tell the size tailleM of the message MSG to send.
To be able to reuse the same packet structure, we disguise a message packet for a specific user as a message to all the users, by sending a key word in REC to indicate that the packet SHOULD be distrubted to all the connected users in the server.
Once the packet is checked by the server, the server sends the message to the all users in a new packet with the same structure as the packet recieved from the client A to :
        1 byte 2 bytes string 2 bytes TailleM bytes
        ---------------------------------------------
        | Code |TailleCA| ClientA | TailleM | MSG |
        ---------------------------------------------
Figure 2-2-2: DATA T2 Packet
## 2.3. Message to a specific user
The process is the same as sending a message to the all users. The only difference is specifying the exact user to send to instead of all the users, for exemple if we were to send a message to a client B, we will have the following format:
        1 byte 2 bytes string 2 bytes TailleM bytes
        ---------------------------------------------
        | Code |TailleCB| ClientB | TailleM | MSG |
        ---------------------------------------------
Figure 2-3-1: DATA T1 Packet
In case the client B doesn’t exist; an error is sent back from the server to the client A (the code will be -1).

1 bytes 126 bytes
---------------------------
| Code | MsgRetour|
---------------------------
Figure 2-3-2: Error Packet
In the case where the client B exist, a packet from the server to the client B is sent. The format is same as the packet from the client A to the server:

    1 byte 2 bytes string 2 bytes TailleM bytes
        ---------------------------------------------
        | Code |TailleCA| ClientA | TailleM | MSG |
        ---------------------------------------------
Figure 2-3-3: DATA T2 Packet
# 3. The private connection
## 3.1. Description
The private connection consists of connecting two clients without them sharing their IP address. The two clients A and B connect each with a new socket to the server: the client A with a socket SA and the the client B with socket SB. After an authentification step, the server transfer all the bytes read from SA to SB and vice versa. After this authentification step, the two clients use this connection “without control”. Everything have to pass like if it’s a normal TCP connection between A and B.
The protocol must allow the clients to make private requests connections and to accept or refuse incoming private requests.
3.2. Process with packets
We have two clients : the client A and the client B. They are already connected to the server and A wants to establish a private connection with the client B.
The client A starts by connecting to the server with this packet :
        1 byte 2 bytes n bytes 2 bytes m bytes
        ------------------------------------------
        | Code | n | ClientA | m | ClientB |
        ------------------------------------------
Figure 3-2-1: Private Connecting Packet
Normally, a new connection is establish by the packet described in the part 2.1. but as the client A informations are already in the server, we can use this packet to establish the connection with a new socket and inform the server of the private request to the client B.
Once the server receive this packet, it MUST save the new socket for the client A and send the request to the client B with the following format:
        1 byte 2 bytes m bytes
        -------------------------
        | Code | m | ClientA |
        -------------------------
Figure 3-2-2: DATA T3 Packet
If the client B doesn’t exist, an error from the server to the client A is returned with the code ‘-1’, the same case as the chapter 2.3
The client B have two possibilities:
1- Accept the request:
The client B connect to the server and then establish a new connection. To inform the server that he accepted the private connection request, the client B send the same packet format that he received from the server, but with the receiver and the sender reversed :
        1 byte 2 bytes m bytes 2 bytes n bytes
        ------------------------------------------
        | Code | m | ClientB | n | ClientA |
        ------------------------------------------
Figure 3-2-3: ACK T2 Packet
The server informs the Client A that a connection with client B was successfully established, therefore Client A can send data on this connection without following a specific protocol.
2- Refuse the request :
The client B declines the private connection request by sending the following packet:
        1 byte 2 bytes m bytes
        -------------------------
        | Code | m | ClientA |
        -------------------------
Figure 3-2-4: ACK T3 Packet
To avoid any pending connections, the client B sends the response to the server without launching a new connection. When the server receives the response, it redirects an ACK packet to the client A:
   1 byte 126 bytes
        -----------------
        | Code | MSG |
        -----------------
Figure 3-2-4: ACK T1 Packet
After that, the server close properly the two connections.

# Packets Formats
      Type	Op #	Format without header

        1 byte 2 bytes string
        -----------------------------------
   Connecting | 0 | NB | Pseudonyme |
        -----------------------------------
1 byte 2 bytes m bytes 2 bytes m bytes
    --------------------------------------------------
   Private	| 3 | m | ASKER | m	| REC |
  Connecting --------------------------------------------------

        2 bytes 2 bytes string 2 bytes string
        ------------------------------------------------
   DATA T1 | 1 | NBREC | REC | NB | MSG |
        ------------------------------------------------
        2 bytes 2 bytes string 2 bytes string
        --------------------------------------------------
   DATA T2 | 2 | NBS | SENDER | NB | MSG |
        --------------------------------------------------

        1 byte 2 bytes string
        ----------------------------
   DATA T3 | 3 | m | Client |
        ----------------------------

        1 byte string
        ---------------------
   ACK T1	| 10/11/13 | Msg |
        ---------------------

        1 byte 2 bytes string 2 bytes string
        ---------------------------------------------------
   ACK T2 | 12 | m | ClientA | m | ClientB |
        ---------------------------------------------------

        1 byte 2 bytes string
        -------------------------------
   ACK T3 | 13 | m | Client |
        -------------------------------

        1 byte string
        -------------------------
   ERROR | -1/-2/-3 | ErrMsg |
        -------------------------
Codes
Value	Meaning
0	connection to the server (part 2.1)
1	Send a message on an established connection
2	Receive a message from a client
3	Request to establish a private connection

# ACK Codes
Value	Meaning
10	connection was established to the server
11	connection was not established to the server
12	Private connection was established
13	Private connection not established
# Error Codes
Value	Meaning
-1	The client doesn’t exist
-2	Packet format was not respected
-3	Unexpected error
# Authors' Addresses

Angelica Amine
email: aamine@etud.u-pem.fr

Mohamed Yassine Yahyaoui
email: myahyao01@etud.u-pem.fr