Authors: Angelica Amine, Mohamed Yassine Yahyaoui
Date : February 2021
UGE

ChatOS

Abstract

ChatOs is a discussion service between multiple users using the same server applying a predefined protocol without sharing users’ IP address.

Status of this Memo

This request for comment summarize the protocol to be implemented in the different packets used for communication between the user and the client.
This document explains also the decisions behind the structure of the packets.

# 1. Introduction
ChatOs protocol purpose is to allow multiple and private communication between users without the need to expose their IP address, the protocol applied and described below is a simplified version of a chat server.

All the packets exchanged in this protocol uses the Transmission Control Protocol, thus packets availability are handled internally.

ChatOs allow three main operations :
- send a message to all the users
- send a message to a specific user
- start private connection with another user

To be able to use any operation, a connection with a server that uses the same protocol MUST be established beforehand.

## 1.1. Requirements notation
This document occasionally uses terms that appear in capital letters.

When the terms "MUST", "SHOULD", "RECOMMENDED", "MUST NOT", "SHOULD NOT", and "MAY" appear capitalized, they are being used to indicate particular requirements of this specification.

A discussion of the meanings of these terms appears in [RFC2119].

## 1.2. Terminology
We describe in this section the terminology used in the protocol.

UTF8
The UTF8 is set as the default charset used in ChatOS.
All requests and packets MUST use this charset unless	mentioned	otherwise in the RFC.

\all
A ChatOS command used by the client side, followed by the user	message, it sends the message to all the other clients connected	to the same server.
User MUST write it at the beginning of line for the command to
be valide.

\pm
A ChatOS command used by the client side, followed by another
clientID then the message to send.
the clientID to send to MUST already be connected to the server.

\cnt
A ChatOS command used by the client side, followed by another
clientID .
It sends a request for establishing a private connection with	another user.

Request
A packet containing data sent from the client to the server.
Starts with request code, size of the ClientId followed by the
client ID, then the size of data zone followed by the data zone.

Ack
A response from the server to the client after receiving a	request.
Composed of a packet code of 2 bytes, and a message zone of 126
bytes.

Packet Code
A code in the start of the packet, coded on 2 bytes, indicates	the purpose or the state of the packet.

# 2. Connecting to the server and first requests
## 2.1. Connection to the server
The first step consists of a client connecting to the server.
For this, a client sends a connecting packet that follows this format :

2 bytes 2 bytes	string
-----------------------------------------
| Code | NB | Pseudonyme |
-----------------------------------------
The code field is an integer coded on 2 bytes, which represents the type of the packet that the server receive, in this case the code is “1” .
The nb field is an integer on 2 bytes which represents the size of the next field : the clientID , a string which is the pseudonyme of the client.

To this request, the server returns an ACK packet to let the client know if connection was established successfully or not.

2 bytes 126 bytes
---------------------------
| Code | MsgRetour|
---------------------------
The code field is an integer coded on 2 bytes which check if the received packet from the client is valid or not.
This field is followed by the message field which represents the reply of the server, we allow a fixed value of 126 bytes, to describe a short error/success message.
If the connection was successfully established then the code is “10”.
if the ClientID already used by another client, then the connection fails with the code “11”.
For any other error that may occurs while connecting, the code “12” is returned, with the return message specifying the cause .
## 2.2. Public message to all users

Once the client is connected to the server, it could to do one the following instructions : send message to all users or send message to a specific user. In this we going to describe the public message process to all users.
We going to consider a client A which want send a message to all users. First, the client A sends to the server a connecting packet that follows this format :

        2 bytes	string 2 bytes 1000 bytes
        -------------------------------------------
        | Code | ClientA | TailleM | MSG |
        -------------------------------------------
The code field is an integer coded on 2 bytes which check if the client A sends a message to all users or for a specific user: as a consequence, this field could have two possible values. The next field is a string which correspond to the pseudonyme of the sender client A. At the end, the packet contains the size message field an integer represented on 2 bytes followed by the message field a string a represented on 1000 bytes on max.
To this request, the server returns an ACK packet to let the client know if message was received in the server or not. The packet have the same representation than ACK packet describes in the part 2.1. for the connection. The only difference is the fact that we check is message is valid or not.
2 bytes	126 bytes
---------------------------
| Code |	MsgRetour	|
---------------------------
Once the packet is checked by the server, the server sends the message to the all users in a new packet which have the same representation that the packet from the client A to the :
        2 bytes	string 2 bytes 1000 bytes
        -------------------------------------------
        | Code | ClientA | TailleM | MSG |
        -------------------------------------------
## 2.3. Message to a specific user
The process is the same as to send to the all users. The only difference is the fact that we specified a field in our packet from the client A the pseudonyme of the client B (the recever). As the result, we have the following format:
        2 bytes	string 2 bytes 1000 bytes
        -------------------------------------------
        | Code | ClientB | TailleM | MSG |
        -------------------------------------------
So like for the all users process, an ACK packet is send from the server to the client A for the same reasons like specified in the part 2.2.
At the end, a packet from the server to the client B is send. The format is same as the pack from the client A to the server instead of the string gived is the client A pseudonyme (the sender):
        2 bytes	string 2 bytes 1000 bytes
        -------------------------------------------
        | Code | ClientA | TailleM | MSG |
        -------------------------------------------

# 3. The private connexion